## Slide 1: Arduino for Robots
Seminars at RSSC.org
Sergei Grichine
slg@quakemap.com

## Slide 2: Agenda
Why Arduino
Common boards – Uno, Mega, Mini, Leonardo and just a chip
Precautions – power, loads
Tools – IDE, logic analyzer, USB/Serial,
Arduino in Robot Architecture
Code:
  Highlights of functions
  Making a library
  Using interrupts to read encoders
  Driving a motor via an H-Bridge
  Multitasking
  Serial communication to a PC
  I2C communication

## Slide 3: Why Arduino
Well designed cheap hardware
Insanely simple programming at the beginning
Friendly IDE – “keep it simple-stupid!”
Exceptional documentation
Community support, samples, forums, experts
Have a question? Just google it!

## Slide 4: Common boards: Uno

## Slide 5: Common boards: Mega 2560

## Slide 6: Common boards: Mini v05

## Slide 7: A no-board solution – just an ATmega328 chip

## Slide 11: Diavolino - also just-a-chip

## Slide 13: Precautions – power, loads
Vin: UNO – 7 to 10V Mega – maybe to 12V
2.1mm power plug (Fry’s has it)
the plug must be "centre positive", that is, the middle pin of the plug has to be the + connection.
250ma or more rated power adapter
Direct feed – 5V stabilized - can’t be used when Vin connected

## Slide 14: Precautions – loads
40ma per pin, total up to 200ma
Be Nice to your Arduino – divide the above by 2… or 4
For a LED, use 100 Ohm or larger resistor in series
No recent (well over 2 years now) Arduino has a built-in resistor on Pin 13.
Google “Arduino pin current”

## Slide 15: Precautions
A must read:
Google “10 Ways to Destroy An Arduino”

## Slide 16: Tools –

## Slide 17: Tools – ICSP programmer
download bootloader to EEPROM
debug using Eclipse and other tools
Google:
“arduino icsp debugging”

## Slide 18: Tools: Logic Analyzer
saleae.com
Designed & Manufactured in beautiful San Francisco

## Slide 19: saleae.com Designed & Manufactured in beautiful San Francisco

## Slide 20: Arduino in Robot Architecture
Not much power – 16 MHz crystal, close to 16 MIPS
8-bit AVR instruction set
Uno / ATmega328
  Flash Memory: 32 KB of which 0.5 KB used by bootloader
  SRAM: 2 KB (a.k.a. RAM)
  EEPROM: 1 KB (persistent storage for settings)
Mega:
  Flash Memory: 256 KB of which 8 KB used by bootloader
  SRAM: 8 KB
  EEPROM: 4 KB

## Slide 21: Roles
Single controller for a small robot

## Slide 22: Roles
Functional controller – servo, drive, sensors, lights, animation, display
High Level Controller (PC, Beaglebone, Android)
Sensor Controller
Tank Drive Controller
Arm Controller
Head Animation Controller
USB to Serial

## Slide 26: Role - Communication controller
High Level Controller (PC, Beaglebone, Android)
Sensor Controller
Tank Drive Controller
Arm Controller
Head Animation Controller
I2C
Communication Controller
USB to Serial
I2C

## Slide 27: Code tips
Not C++, Not quite Java – but close
Google “arduino reference”
Functions - http://arduino.cc/en/Reference/HomePage
http://arduino-info.wikispaces.com/HOME

## Slide 28: Code tour
Code:
  Highlights of functions
  Making a library
  Using interrupts to read encoders
  Serial communication to a PC
  Driving a motor via an H-Bridge
  Multitasking
  I2C communication

## Slide 29: Making a Library
Explore existing
Think of a good interface
Make your own

## Slide 30: Arduino for Robots
Seminars at RSSC.org
Sergei Grichine
slg@quakemap.com